## Slide 1: Electrical Flow Routing for LEO Satellite Constellations
A Circuit-Inspired Approach to ISL Routing
Nicholas Zayfman (nzayfma1@jh.edu)

## Slide 2: Problem Statement
Mega-constellation scale:
  Starlink: 5,000+ satellites (projected 12,000+)
  OneWeb: 648 satellites
  Amazon Kuiper: 3,236 satellites
Traditional routing limitations:
  Dijkstra/OSPF: Single-path, centralized
  No natural multi-path discovery for load balancing
  Poor scalability beyond 10,000+ nodes
  Slow adaptation to dynamic topology changes

## Slide 3: Core Hypothesis
Central insight: Electrons naturally load-balance across parallel paths based on resistance.
  Can we leverage this physics-inspired approach for optimal traffic routing?
Key properties of electrical flow:
  Automatic distribution through parallel paths
  Follows principle of least energy dissipation
  Inherently distributed and self-balancing
  Based on proven physical laws, not heuristics

## Slide 4: The Circuit-Network Analogy
Network Concept | Electric Analog
Satellite Node | Electrical Junction
Inter-Satellite Links (ISL) | Resistor
Data Traffic | Electric Circuit
Source Satellite | +V Terminal
Destination Satellite | Ground (0V)
Routing Decision | Natural Current Distribution

## Slide 5: Mathematical Foundation
Resistance Mapping:
  R(link) = α·(latency) + β·(1/capacity)
  Higher latency → Higher resistance (avoid slow links)
  Higher capacity → Lower resistance (prefer bandwidth)
  α, β control optimization trade-offs
Kirchhoff's Current Law (KCL):
  At every intermediate node: ∑I_in = ∑I_out
  Conservation of flow (no data creation/destruction)
Ohm's Law:
  V_u - V_v = I_uv · R_uv
  Voltage difference drives current through resistance
Laplacian System:
  L · V = b
  L = Graph Laplacian matrix (conductances)
  V = Node voltage vector (unknowns to solve)
  b = Current injection vector (+1 source, -1 destination)
Flow Computation:
  Flow(u→v) = Conductance(u,v) · (V_u - V_v)

## Slide 6: Algorithm Advantages
Natural Load Balancing:
  Current automatically splits across parallel paths proportional to conductances
Optimal Distribution:
  Minimizes energy dissipation, equivalent to optimal flow distribution
Fast Computation:
  Sparse linear system, O(n log n) with Spielman-Teng solvers
    https://link.springer.com/chapter/10.1007/978-3-642-13562-0_2
Physical Realism:
  Based on Maxwell's equations, not ad-hoc heuristics

## Slide 7: Implementation Details
LEO Constellation Module:
  Real Starlink TLE data ingestion
  SGP4 orbital propagation
  FSO link budget calculations (next-gen physical layer)
  Time-varying network topology builder
Electrical Flow Router Module:
  Laplacian matrix construction
  Sparse linear solver (scipy.sparse.linalg)
  Edge flow computation via Ohm's law
  Path extraction and comparison engine

## Slide 8: Evaluation Metrics
Performance Metrics:
  End-to-end latency (ms)
  Path capacity (Gbps)
  Number of parallel paths discovered
  Computation time (ms)
Comparison Baseline:
  Dijkstra shortest path algorithm
  Single-path optimal latency
  No load balancing capability
Other Comparisons:
  Open Shortest Path First (OSPF)
  Equal-Cost Multi-Path (ECMP)
  Other more recent contributions utilizing SDN.
Scalability Tests:
  Constellation sizes: 50, 100, 200, 500, 1000 satellites
  Memory usage and convergence analysis

## Slide 9: Thank you
Questions?

## Slide 10: Copyright The Johns Hopkins University 2025. All rights reserved.