## Slide 1: Electrical Flow Routing for LEO Satellite Constellations
A Circuit-Inspired Approach to ISL Routing
Nicholas Zayfman (nzayfma1@jh.edu)

## Slide 2: Problem Statement
Mega-constellation scale:
  Starlink: 5,000+ satellites (projected 12,000+)
  OneWeb: 648 satellites
  Amazon Kuiper: 3,236 satellites
Traditional routing limitations:
  Dijkstra/OSPF: Single-path, centralized
  No natural multi-path discovery for load balancing
  Poor scalability beyond 10,000+ nodes
  Slow adaptation to dynamic topology changes

## Slide 3: Core Hypothesis
Central insight: Electrons naturally load-balance across parallel paths based on resistance.
  Can we leverage this physics-inspired approach for optimal traffic routing?
Key properties of electrical flow:
  Automatic distribution through parallel paths
  Follows principle of least energy dissipation
  Inherently distributed and self-balancing
  Based on proven physical laws, not heuristics

## Slide 4: Not a new concept but a new application
Quanta Magazine Article: "Researchers Achieve 'Absurdly Fast' Algorithm for Network Flow" (2022)
  https://www.quantamagazine.org/researchers-achieve-absurdly-fast-algorithm-for-network-flow-20220608/
"Electrical flows, Laplacian systems, and faster approximation of maximum flow in undirected graphs" (2013)
  https://people.csail.mit.edu/madry/docs/maxflow.pdf
"Electric Routing and Concurrent Flow Cutting" (2009)
  https://link.springer.com/chapter/10.1007/978-3-642-10631-6_80
"Robust Routing Using Electrical Flows" - Google Research (SIGSPATIAL 2021)
  https://dl.acm.org/doi/10.1145/3567421

## Slide 5: Multicasting and Bit error?
Multicasting
  Superposition of Independent Flows (Leverages linearity of electrical circuits)
    Since the Laplacian system is linear, we can solve for multiple destinations at the same time.
    Set source node = +F
    Set each destination k: = -F/n (where n = num of destinations)
    The resulting flow naturally distribute to all destinations
Bit Error Rate (BER) / Link Quality
  Adjust the resistance formula to include link quality – Higher BER -> higher resistance -> less flow routed through that link.
  Monitor actual BER on each link and update resistance values in real-time to take account, so flow will automatically redistribute away from degraded links.

## Slide 6: The Circuit-Network Analogy
Network Concept | Electric Analog
Satellite Node | Electrical Junction
Inter-Satellite Links (ISL) | Resistor
Data Traffic | Electric Circuit
Source Satellite | +V Terminal
Destination Satellite | Ground (0V)
Routing Decision | Natural Current Distribution

## Slide 7: Mathematical Foundation
Resistance Mapping:
  R(link) = α·(latency) + β·(1/capacity)
  Higher latency → Higher resistance (avoid slow links)
  Higher capacity → Lower resistance (prefer bandwidth)
  α, β control optimization trade-offs
Kirchhoff's Current Law (KCL):
  At every intermediate node: ∑I_in = ∑I_out
  Conservation of flow (no data creation/destruction)
Ohm's Law:
  V_u - V_v = I_uv · R_uv
  Voltage difference drives current through resistance
Laplacian System:
  L · V = b
  L = Graph Laplacian matrix (conductances)
  V = Node voltage vector (unknowns to solve)
  b = Current injection vector (+1 source, -1 destination)
Flow Computation:
  Flow(u→v) = Conductance(u,v) · (V_u - V_v)

## Slide 8: Algorithm Advantages
Natural Load Balancing:
  Current automatically splits across parallel paths proportional to conductances
Optimal Distribution:
  Minimizes energy dissipation, equivalent to optimal flow distribution
Fast Computation:
  Sparse linear system, O(n log n) with Spielman-Teng solvers
    https://link.springer.com/chapter/10.1007/978-3-642-13562-0_2
Physical Realism:
  Based on Maxwell's equations, not ad-hoc heuristics

## Slide 9: Implementation Details
LEO Constellation Module:
  Real Starlink TLE data ingestion
  SGP4 orbital propagation
  FSO link budget calculations (next-gen physical layer)
  Time-varying network topology builder
Electrical Flow Router Module:
  Laplacian matrix construction
  Sparse linear solver (scipy.sparse.linalg)
  Edge flow computation via Ohm's law
  Path extraction and comparison engine

## Slide 10: Simulation Framework
Orbital Propagation
  SGP4 model with Two-Line Element (TLE) data from CelesTrak
  True Equator Mean Equinox (TEME) reference frame
  ~1 km accuracy at epoch, grows 1-3 km/day
Free-Space Optical Link Budget
  Wavelength: 1550 nm (C-band)
  Transmit power: +20 dBm
  Receiver sensitivity: -40 dBm
  Free-space path loss: L_space = 20·log₁₀(4π·d/λ)
  Geometric constraints: 5000 km max distance, 25° min elevation
Test Network Topology
  100 satellites (nodes)
  1,426 bidirectional inter-satellite links
  Average degree: 28.52
  Network diameter: 6 hops
  Latency: 3.3 ms per 1000 km
  Link capacity: 10-100 Gbps estimated from SNR
Resistance Model Parameters
  α (latency weight) = 1.0
  β (capacity weight) = 1.0
  λ_norm = 100 ms (normalization)
  κ_norm = 10 Gbps (normalization)

## Slide 11: Performance Comparison
Multi-path discovery: 5 parallel paths vs. single paths for all baselines
Latency penalty: Only 2.6% increase over Dijkstra's optimal (62.64 vs 61.04 ms = 1.6 ms difference)
Computation time: 14.07 ms faster than OSPF (19.30 ms), acceptable for near-real-time routing in predictable LEO topologies
Comparable capacity: Maintains same 10 Gbps capacity as baselines

## Slide 12: Load Balancing Analysis
Effective Paths: 568.69
  Derived from Herfindahl-Hirschman Index
  Hundreds of effective paths vs. single-path baseline methods
Gini Coefficient: 0.526
  Moderate flow concentration
  Not perfectly uniform, but substantially better than single-path
  0 = perfect equality, 1 = perfect inequality
Normalized Entropy: 0.930
  On 0-1 scale, confirms flow well-dispersed across network
  High entropy = traffic spread across many paths
Max/Avg Flow Ratio: 7.95
  No single link overwhelmingly congested
  Some edges carry higher loads, but distribution is balanced

## Slide 13: Conclusion & Future Work
Key Findings
  Electrical flow routing discovers significantly more parallel paths than baseline algorithms
  Load distribution metrics indicate effective exploitation of network path diversity
Advantage over traditional approach
  Natural multi-path discovery without explicit computation
  Automatic load balancing through circuit physics
  Resilience to link failures and congestion
  Single optimization framework handles latency + capacity trade-offs
Future Research
  Larger Constellations, Longer simulation time frames, and Multiple orbital shells/inclination
  Better enhanced resistance modeling with statistical analysis
  Advanced comparisons (GNN + DQN, SDN, etc.)
  Realistic Traffic Patterns
  More in depth model
Github Repo
  https://github.com/nickyduesxd/ElectroFlow.git

## Slide 14: Thank you
Questions?

## Slide 15: Copyright The Johns Hopkins University 2025. All rights reserved.